## Slide 1
Computer Architecture: A Constructive Approach
Sequential Circuits
Derek Chiou
The University of Texas at Austin
Taken (with permission) from
Arvind and collaborators*
Computer Science & Artificial Intelligence Lab.
Massachusetts Institute of Technology
* Joel Emer, Li-Shiuan Peh, Murali Vijayaraghavan, Asif Khan, Abhinav Agarwal, Myron King

## Slide 2: Content
Introduce sequential circuits as a way of saving area
  Edge-triggered Flip-flop
  Register
New Bluespec concepts
  state elements
  rules and actions for describing dynamic behavior
  modules and methods

## Slide 3: Combinational 32-bit multiply
function Bit#(64) mul32(Bit#(32) a, Bit#(32) b);
Bit#(32) prod = 0; Bit#(32) tp = 0; for(Integer i = 0; i < 32; i = i+1) begin Bit#(32) m = (a[i]==0)? 0 : b; Bit#(33) sum = add32(m,tp,0); prod[i] = sum[0]; tp = truncateLSB(sum); end return {tp,prod}; endfunction
Combinational circuit uses 31 add32 circuits
We can reuse the same add32 circuit if we can store the partial results in some storage device, e.g., register

## Slide 4: Combinational circuits
OpSelect
- Add, Sub, ...
- And, Or, Xor, Not, ...
- GT, LT, EQ, Zero, ...
Result
Comp?
A
B
ALU
Sel
O
A0
A1
An-1
Mux
.
.
.
lg(n)
Sel
O0
O1
On-1
A
Demux
.
.
.
lg(n)
A
Decoder
.
.
.
O0
O1
On-1
lg(n)
Such circuits have no cycles (feedback) or state elements

## Slide 5: A simple synchronous state element
ff
Q
D
C
C
D
Q
Metastability possible if data available too late
Data is sampled at the rising edge of the clock
Edge-Triggered Flip-flop

## Slide 6: Flip-flops with Write Enables
ff
Q
D
C
EN
C
D
Q
EN
ff
Q
D
C
EN
0
1
ff
Q
D
C
EN
dangerous!
Data is captured only if EN is on
Notes: Why dangerous?
Glitches

## Slide 7: Registers
Register: A group of flip-flops with a common
clock and enable
Register file: A group of registers with a common
clock, input and output port(s)
ff
D
ff
D
ff
D
ff
D
ff
D
ff
D
ff
D
ff
Q
Q
Q
Q
Q
Q
Q
Q
D
C
En

## Slide 8: Register Files
ReadData1
ReadSel1
ReadSel2
WriteSel
Register
file
2R + 1W
ReadData2
WriteData
WE
Clock
Reads are combinational and not affected by the write until the next clock cycle
register 1
WSel
C
register 0
WData
WE
RSel2
RData2
RSel1
RData1

## Slide 9: Register Files and Ports
Ports are expensive multiplex single port for read & write
ReadData1
ReadSel1
ReadSel2
WriteSel
Register
file
2R + 1W
ReadData2
WriteData
WE
ReadData
ReadSel
R/WSel
Register
file
1R + 1R/W
R/WData
WE

## Slide 10: We can build useful and compact circuits using registers
Circuits containing state elements are called sequential circuits

## Slide 11: Expressing a loop using registers
int s = s0;
for (int i = 0; i < 32; i = i+1) { s = f(s); } return s; C-code
sel
< 32
0
notDone
+1
i
en
sel = start
en = start | notDone
s0
f
sel
s
en
We need two registers to hold s and i values from one iteration to the next.
These registers are initialized when the computation starts and updated every cycle until the computation terminates

## Slide 12: Expressing sequential circuits in Bluespec
Sequential circuits, unlike combinational circuits, are not expressed structurally (as wiring diagrams) in Bluespec
For sequential circuits a designer defines:
  State elements by instantiating modules
Reg#(Bit#(32)) s <- mkRegU();
Reg#(Bit#(6)) i <- mkReg(32);
  Rules which define how state is to be transformed atomically
  rule step if (i < 32); s <= f(s); i <= i+1; endrule
make a 32-bit register which is uninitialized
make a 6-bit register with initial value 32
the rule can execute only when its guard is true
actions to be performed when the rule executes

## Slide 13: Rule Execution
< 32
notDone
+1
sel
0
i
en
sel = start
en = start | notDone
f
s0
sel
s
en
Reg#(Bit#(32)) s <- mkRegU();
Reg#(Bit#(6)) i <- mkReg(32);
rule step if (i < 32); s <= f(s); i <= i+1; endrule
When a rule executes:
  all the registers are read at the beginning of a clock cycle
  the guard and computations to evaluate the next value of the registers are performed
  at the end of the clock cycle registers are updated iff the guard is true
Muxes are need to initialize the registers

## Slide 14: Multiply using registers
function Bit#(64) mul32(Bit#(32) a, Bit#(32) b);
Bit#(32) prod = 0; Bit#(32) tp = 0; for(Integer i = 0; i < 32; i = i+1) begin Bit#(32) m = (a[i]==0)? 0 : b; Bit#(33) sum = add32(m,tp,0); prod[i] = sum[0]; tp = truncateLSB(sum); end return {tp,prod}; endfunction
Need registers to hold a, b, tp, prod and i
Update the registers every cycle until we are done
Combinational version

## Slide 15: Sequential multiply
Reg#(Bit#(32)) a <- mkRegU();
Reg#(Bit#(32)) b <- mkRegU();
Reg#(Bit#(32)) prod <-mkRegU(); Reg#(Bit#(32)) tp <- mkRegU();
Reg#(Bit#(6)) i <- mkReg(32);
rule mulStep if (i < 32); Bit#(32) m = (a[i]==0)? 0 : b; Bit#(33) sum = add32(m,tp,0); prod[i] <= sum[0]; tp <= sum[32:1];
i <= i+1; endrule
state elements
a rule to describe the dynamic behavior
The rule won’t fire until i is set to value smaller than 32
similar to the loop body in the combinational version
Notes: Need to provide values to a and b at some point.

## Slide 16: Dynamic selection requires a mux
a[i]
a
i
a[0],a[1],a[2],…
a
>>
0
when the selection indices are regular then it is better to use a shift operator (no gates!)

## Slide 17: Replacing repeated selections by shifts
Reg#(Bit#(32)) a <- mkRegU();
Reg#(Bit#(32)) b <- mkRegU();
Reg#(Bit#(32)) prod <-mkRegU(); Reg#(Bit#(32)) tp <- mkRegU();
Reg#(Bit#(6)) i <- mkReg(32);
rule mulStep if (i < 32); Bit#(32) m = (a[0]==0)? 0 : b;
a <= (a >> 1); Bit#(33) sum = add32(m,tp,0); prod <= {sum[0], (prod >> 1)[30:0]}; tp <= sum[32:1];
i <= i+1; endrule

## Slide 18: Circuit for Sequential Multiply
bIn
b
a
i
== 32
0
done
+1
prod
result (low)
<<
[30:0]
aIn
<<
31:0
tp
s1
s1
s1
s2
s2
s2
s2
s1
s1 = start_en
s2 = start_en | !done
result (high)
31
0
add
0
0
32:1
0

## Slide 19: Circuit analysis
Number of add32 circuits has been reduced from 31 to one, though some registers and muxes have been added
The longest combinational path has been reduced from 31 serial add32’s to one add32 plus a few muxes
The sequential circuit will take 31 clock cycles to compute an answer

## Slide 20: Modules
We often package sequential circuits into modules to hide the details

## Slide 21: Multiply Module
rdy
en
Bit#(32)
Bit#(64)
rdy
start
result
Multiply
module
Bit#(32)
interface Multiply;
method Action start
(Bit#(32) a, Bit#(32) b);
method Bit#(64) result();
endinterface
A module in Bluespec in like an object in an object-oriented language and can only be manipulated via the methods of its interface
However, unlike software, a method in Bluespec can be applied only when it is “ready”
Furthermore, application of an action method, i.e., a method that changes the state of a module, is indicated by asserting the associated enable wire

## Slide 22: Multiply Module
module mkMultiply32 (Multiply);
Reg#(Bit#(32)) a <- mkRegU();
Reg#(Bit#(32)) b <- mkRegU();
Reg#(Bit#(32)) prod <-mkRegU(); Reg#(Bit#(32)) tp <- mkRegU();
Reg#(Bit#(6)) i <- mkReg(32);
rule mulStep if (i != 32);
Bit#(32) m = (a[0]==0)? 0 : b; Bit#(33) sum = add32(m,tp,0); prod <= {sum[0], (prod >> 1)[30:0]}; tp <= truncateLSB(sum); a <= a >> 1; i <= i+1;
endrule
method Action start(Bit#(32) aIn, Bit#(32) bIn)
if (i == 32);
a <= aIn; b <= bIn; i <= 0; tp <= 0; prod <= 0;
endmethod
method Bit#(64) result() if (i == 32);
return {tp,prod};
endmethod endmodule
State
Internal
behavior
External
interface
method guards

## Slide 23: Module: Method Interface
s1 = start_en
s2 = start_en | !done
== 32
0
done
+1
aIn
bIn
en
rdy
result
rdy
start
result
s1
OR
s1
s2
bIn
b
a
i
prod
result (low)
<<
[30:0]
aIn
<<
31:0
tp
result (high)
add
0
31
0
0
s1
s1
s1
s2
s2
s2
s2
s1
32:1
0

## Slide 24: Polymorphic Multiply Module
rdy
en
Bit#(32)
Bit#(64)
rdy
start
result
Multiply
module
Bit#(32)
implicit conditions
interface Multiply;
method Action start (Bit#(32) a, Bit#(32) b);
method Bit#(64) result();
endinterface
n
#(Numeric type n)
n
Tadd(n,n)
n
n
TAdd#(n,n)
n could be
32, 13, …
The module can easily be made polymorphic

## Slide 25: Sequential n-bit multiply
module mkMultiplyN (MultiplyN#(n));
Reg#(Bit#(n)) a <- mkRegU();
Reg#(Bit#(n)) b <- mkRegU();
Reg#(Bit#(n)) prod <-mkRegU(); Reg#(Bit#(n)) tp <- mkRegU();
let nv = fromInteger(valueOf(n)); Reg#(Bit#(TAdd#(TLog#(n),1))) i <- mkReg(nv);
rule mulStep if (i != nv);
Bit#(n) m = (a[0]==0)? 0 : b; Bit#(Tadd#(n,1)) sum = addN(m,tp,0); prod <= {sum[0], (prod >> 1)[(nv-2):0]}; tp <= truncateLSB(sum); a <= a >> 1; i <= i+1;
endrule
method Action start(Bit#(n) aIn, Bit#(n) bIn) if (i == nv);
a <= aIn; b <= bIn; i <= 0; tp <= 0; prod <= 0;
endmethod method Bit#(Tadd#(n,n)) result() if (i == nv);
return {tp,prod};
endmethod endmodule

## Slide 26: Multiply Module
interface Multiply;
method Action start (Bit#(32) a, Bit#(32) b);
method Bit#(64) result();
endinterface
The same interface can be implemented in many different ways:
  module mkMultiply (Multiply)
  module mkBlockMultiply (Multiply)
  module mkBoothMultiply (Multiply)…

## Slide 27: What Did We Learn?
State
Sequential circuits
  Reduce duplication/area at the cost of speed, additional state, and control
How to implement sequential circuits in Bluespec