## Slide 1
Computer Architecture: A Constructive Approach
Bluespec execution model and concurrent rule scheduling
Derek Chiou, Xiaoyu Ma (TA)
The University of Texas at Austin
Taken (with permission) from
Arvind and collaborators*
Computer Science & Artificial Intelligence Lab.
Massachusetts Institute of Technology
* Joel Emer, Li-Shiuan Peh, Murali Vijayaraghavan, Asif Khan, Abhinav Agarwal, Myron King

## Slide 2: Content
Bluespec execution model
  one-rule-at-a-time semantics
Guard lifting
Concurrent execution of rules
  a semantic view
  Hardware intuition for concurrent execution
In this lecture we would take liberties with Bluespec syntax and ignore type issues

## Slide 3: Bluespec Rule Execution
A Bluespec program consists of state elements and rules, aka, Guarded Atomic Actions (GAA) that operate on the state elements
Application of a rule modifies some state elements of the system in a deterministic manner
  Let s’ = a(s) where s’ represents the state obtained by applying action a to state s
  We can define the application of a rule by either giving a procedure or by describing a hardware circuit to compute the new state
current
state
next
state
values
next state
computation
f
x
f
x
guard
reg en’s
nextState
AND

## Slide 4: Bluespec Execution Model
Repeatedly:
Select a rule to execute
Compute the state updates
Make the state updates
A legal behavior of a Bluespec program can be explained by observing the state updates obtained by applying only one rule at a time
Highly non-deterministic; User annotations can be used in rule selection
One-rule-at-time semantics

## Slide 5: Rule evaluation
rule name e a
a ::= x<= e
| a ; a
| if (e) a
| t = e ; a
e ::= c | t | x | op(e,e)
evalA :: (Bindings, State, a) -> (Bindings, StateUpdates)
evalE :: (Bindings, State, e) -> Value
guard
action
simplest action: register assignment
conditional action
binding
parallel actions
expression
register values
variable bindings

## Slide 6: Legal Bluespec rules
A legal Bluespec rule does not contain multiple assignments to the same state element or combinational cycles
Examples: legal?
rule ra if (z>10);
x <= x+1; endrule
rule rb;
x <= x+1; if (p) x <= 7 endrule
rule rc;
x <= y+1; y <= x+2 endrule
rule rd;
t1 = f(t2); t2 = g(t1); x <= t1; endrule
no
yes
yes
no
In general the legality of a rule can be determined only at run time.

## Slide 7: Guard Lifting

## Slide 8: Making guards explicit
rule foo if (True);
if (p) fifo.enq(8);
r <= 7;
endrule
rule foo if ((p && fifo.notFull) || !p);
if (p) fifo.enq(8);
r <= 7;
endrule
Effectively, all implicit conditions (guards) are lifted and conjoined to the rule guard

## Slide 9: Implicit guards (conditions)
rule <name> if (<guard>); <action>; endrule
make implicit guards explicit
m.gB(<exp>) when m.gG
<action> ::= r <= <exp>
| if (<exp>) <action>
| <action> ; <action>
| m.g(<exp>)
| t = <exp>
<action> ::= r <= <exp>
| if (<exp>) <action>
| <action> when (<exp>)
| <action> ; <action>
| m.g(<exp>)
| t = <exp>

## Slide 10: Guards vs If’s
A guard on one action of a parallel group of actions affects every action within the group
(a1 when p1); a2
==> (a1; a2) when p1
A condition of a Conditional action only affects the actions within the scope of the conditional action
(if (p1) a1); a2
p1 has no effect on a2 ...
Mixing ifs and whens
(if (p) (a1 when q)) ; a2
 ((if (p) a1); a2) when ((p && q) | !p)
 ((if (p) a1); a2) when (q | !p)

## Slide 11: Guard Lifting rules
All the guards can be “lifted” to the top of a rule
  (a1 when p) ; a2 
  a1 ; (a2 when p) 
  if (p when q) a 
  if (p) (a when q) 
  (a when p1) when p2 
  x <= (e when p) 
similarly for expressions ...
  Rule r (a when p) 
  (a1 ; a2) when p
  (a1 ; a2) when p
  (if (p) a) when q
  (if (p) a) when (q | !p)
  a when (p1 & p2)
  (x <= e) when p
  Rule r (if (p) a)

## Slide 12
Bluespec provides a primitive (impCondOf) to make guards explicit and lift them to the top
From now on we will assume that all guards have been lifted to the top in every rule.

## Slide 13: Concurrent scheduling: Semantic view
Suppose rule r1 a1 and rule r2 a2 are legal rules. r1 and r2 are concurrently schedulable, iff,
  rule r12 (a1;a2) is legal
  for all s, (a1;a2)(s) = a1(a2(s)) or a2(a1(s))
Concurrent scheduling of two rules, when permitted, can be expressed as a new derived rule, i.e., r12

## Slide 14: Example 1
{x0,y0,30} ra {x0+1,y0,30} rb {x0+1,y0+2,30}
{x0,y0,30} rb {x0,y0+2,30} ra {x0+1,y0+2,30}
{x0,y0,30} ra_rb {x0+1,y0+2,30}
{x0,y0,15} ra {x0+1,y0,15} rb {x0+1,y0,15}
{x0,y0,15} rb {x0,y0,15} ra {x0+1,y0,15}
{x0,y0,15} ra_rb {x0+1,y0,15}
Parallel execution behaves like
ra < rb (i.e., rb(ra(s))
= rb < ra (i.e., ra(rb(s))
rule ra if (z>10);
x <= x+1;
endrule
rule rb if (z>20);
y <= y+2;
endrule
rule ra_rb;
if (z>10) x <= x+1;
if (z>20) y <= y+2;
endrule

## Slide 15: Example 2
{x0,y0,30} ra {y0+1,y0,30} rb {y0+1,y0+1+2,30}
{x0,y0,30} rb {x0,x0+2,30} ra {x0+2+1,x0+2,30}
{x0,y0,30} ra_rb {y0+1,x0+2,30}
rule ra if (z>10);
x <= y+1;
endrule
rule rb if (z>20);
y <= x+2;
endrule
rule ra_rb;
if (z>10) x <= y+1;
if (z>20) y <= x+2;
endrule
Rule ra_rb is legal but does not behave like either ra < rb or rb < ra
Rules ra and rb conflict and can’t be scheduled concurrently

## Slide 16: Example 3
{x0,y0,30} ra {y0+1,y0,30} rb {y0+1,y0+2,30}
{x0,y0,30} rb {x0,y0+2,30} ra {y0+2+1,y0+2,30}
{x0,y0,30} ra_rb {y0+1,y0+2,30}
rule ra if (z>10);
x <= y+1;
endrule
rule rb if (z>20);
y <= y+2;
endrule
rule ra_rb;
if (z>10) x <= y+1;
if (z>20) y <= y+2;
endrule
Rule ra_rb is legal and behaves like ra < rb (i.e., rb(ra(s)))
Rules ra and rb can be scheduled concurrently with the functionality ra < rb

## Slide 17: Example 4
rule ra;
x <= y+1; u <= u+2;
endrule
rule rb;
y <= y+2; v <= u+1;
endrule
rule ra_rb;
x <= y+1; u <=u+2;
y <= y+2; v <=u+1;
endrule
Rule ra_rb is legal but does not behave like either ra < rb or rb < ra
Notice read/write accesses to y can be resolved by ordering ra < rb while accesses to u can be resolved by ordering rb < ra. Since these orderings are contradictory these rules conflict and cannot be scheduled concurrently

## Slide 18: Hardware intuition for concurrent scheduling

## Slide 19: some insight into Concurrent rule firing
There are more intermediate states in the rule semantics (a state after each rule step)
In the HW, states change only at clock edges
Rules
HW
Ri
Rj
Rk
clocks
rule
steps
Ri
Rj
Rk

## Slide 20: Parallel execution reorders reads and writes
In the rule semantics, each rule sees (reads) the effects (writes) of previous rules
In the HW, rules only see the effects from previous clocks, and only affect subsequent clocks
Rules
HW
clocks
rule
steps
reads
writes
reads
writes
reads
writes
reads
writes
reads
writes
reads
writes
reads
writes

## Slide 21: Correctness
Rules are allowed to fire in parallel only if the net state change is equivalent to sequential rule execution
Consequence: the HW can never reach a state unexpected in the rule semantics
Rules
HW
Ri
Rj
Rk
clocks
rule
steps
Ri
Rj
Rk

## Slide 22: Compiling a Rule
f
x
current
state
next
state
d
p
guard
f
x
rule r (f.first() > 0) ;
x <= x + 1 ; f.deq ();
endrule
rdy signals
read methods
next state values
Notes: In a circuit, pi maps to combination logic that looks at the current state and generates a boolean enable signal for this rule
The delta functions is another combination logic that computes the next state value from the current state value. Actually, delta has to compute the control signals to set the state element to the new value

## Slide 23: Combining State Updates: strawman
next state
value
latch
enable
R
OR
p1
pn
d1,R
dn,R
OR
p’s from the rules
that update R
d’s from the rules
that update R
What if more than one rule is enabled?
Notes: After mapping all the rules, we have to combine their logic some how.
For a particular state elemetn like the PC register,
the latch enable is the or the enable signals from all the rules that updates PC.
The actual next state value of PC has to be selected through a multiplexer.
Notice, this circuit only works if only one of these pi signal is asserted at a time

## Slide 24: Combining State Updates
next state
value
latch
enable
R
Scheduler:
Priority
Encoder
OR
f1
fn
p1
pn
d1,R
dn,R
OR
d’s from the rules
that update R
Scheduler ensures that at most one fi is true
p’s from all
the rules
one-rule-at-a-time
scheduler is
conservative
Notes: After mapping all the rules, we have to combine their logic some how.
For a particular state elemetn like the PC register,
the latch enable is the or the enable signals from all the rules that updates PC.
The actual next state value of PC has to be selected through a multiplexer.
Notice, this circuit only works if only one of these pi signal is asserted at a time

## Slide 25: Concurrent scheduling
The Bluespec compiler determines which rules among the rules whose guards are ready can be executed concurrently
It then divides the rules into disjoint sets such that the rules within each set are conflict free
Among conflicting sets of enabled rules it picks one set by some predetermined priority
The designers need to develop intuition about which rules can be executed concurrently and which ones conflict and thus, must be executed one by one

## Slide 26: A compiler test for concurrent rule firing James Hoe, Ph.D., 2000
Let R(r) represent the set of registers a rule r may read
Let W(r) represent the set of registers a rule r may write
Rules ra and rb are conflict free (CF) if
  R(ra)W(rb) =   R(rb)W(ra) =   W(ra)W(rb) = 
Rules ra and rb are sequentially composable (ra<rb) if
  R(rb)W(ra) =   W(ra)W(rb) = 

## Slide 27: Scheduling and control logic
Modules
(Current state)
Rules
d1
p1
Scheduler
f1
fn
p1
pn
Muxing
d1
dn
dn
pn
Modules
(Next state)
cond
action
“CAN_FIRE”
“WILL_FIRE”
Compiler synthesizes a scheduler such that at any given time f’s for only non-conflicting rules are true
Notes: After mapping all the rules, we have to combine their logic some how.
For a particular state elemetn like the PC register,
the latch enable is the or the enable signals from all the rules that updates PC.
The actual next state value of PC has to be selected through a multiplexer.
Notice, this circuit only works if only one of these pi signal is asserted at a time

## Slide 28: What Did We Learn?
The rules of firing Bluespec rules
  One-rule-at-a-time
  When rules can fire concurrently
  Interaction between guards and conditional actions
  Compiler analysis to determine the conflict free property
Compiler generated hardware scheduler
Hardware intuition and implementation