## Slide 1
Computer Architecture: A Constructive Approach
EHRs: Designing modules with concurrent methods
Derek Chiou
The University of Texas at Austin
Taken (with permission) from
Arvind and collaborators*
Computer Science & Artificial Intelligence Lab.
Massachusetts Institute of Technology
* Joel Emer, Li-Shiuan Peh, Murali Vijayaraghavan, Asif Khan, Abhinav Agarwal, Myron King

## Slide 2: Contents
Concurrent module methods
Limitations of the Bluespec model
Extending the model with EHRs: Ephemeral History Registers
Coding FIFOs with different concurrency properties using EHRs
Simultaneous access to several modules

## Slide 3: Elastic pipeline
x
fifo1
inQ
f1
f2
f3
fifo2
outQ
rule stage1 if (True);
fifo1.enq(f1(inQ.first());
inQ.deq(); endrule
rule stage2 if (True);
fifo2.enq(f2(fifo1.first());
fifo1.deq(); endrule
rule stage3 if (True);
outQ.enq(f3(fifo2.first());
fifo2.deq(); endrule
Can these rules fire concurrently?
Need a way to discuss the concurrent properties of method calls

## Slide 4: Notation
For a group of actions {a1,a2,…} and {b1,b2,…}
  {a1, a2,…} CF {b1, b2,…} iff i,j. (ai CF bj)
  {a1, a2,…} < {b1, b2,…} iff
  i,j. ((ai < bj) or (ai CF bj)) and i,j. ai < bj
There exists at least one ai < bj

## Slide 5: Concurrency analysis
rule stage1 if (True);
fifo1.enq(f1(inQ.first));
inQ.deq;
endrule
rule stage2 if (True);
fifo2.enq(f2(fifo1.first));
fifo1.deq;
endrule
Can these rules fire concurrently?
For concurrent scheduling of stage1 and stage2, {fifo1.enq, inQ.first, inQ.deq}
CF/</> {fifo1.first, fifo1.deq, fifo2.enq}
 either {fifo1.enq} CF {fifo1.first, fifo1.deq}
or {fifo1.enq} < {fifo1.first, fifo1.deq}
or {fifo1.enq} > {fifo1.first, fifo1.deq}
Need to analyze FIFOs!

## Slide 6: One-Element FIFO
module mkCFFifo (Fifo#(1, t));
Reg#(t) data <- mkRegU;
Reg#(Bool) full <- mkReg(False);
method Action enq(t x) if (!full);
full <= True; data <= x;
endmethod
method Action deq if (full);
full <= False;
endmethod
method t first if (full);
return (data);
endmethod
endmodule
enq and deq cannot even be enabled together much less fire concurrently!
n
not empty
not full
rdy
enab
rdy
enab
enq
deq
Fifo
module

## Slide 7: Two-Element FIFO
module mkCFFifo (Fifo#(2, t));
Reg#(t) da <- mkRegU();
Reg#(Bool) va <- mkReg(False);
Reg#(t) db <- mkRegU();
Reg#(Bool) vb <- mkReg(False);
method Action enq(t x) if (!vb);
if va then begin db <= x; vb <= True; end
else begin da <= x; va <= True; end
endmethod
method Action deq if (va);
if vb then begin da <= db; vb <= False; end
else begin va <= False; end
endmethod
method t first if (va);
return da;
endmethod
endmodule
Assume, if there is only one element in the FIFO it resides in da
db da
enq and deq can be enabled together
Do enq and deq conflict?
yes
Both read/write the same elements and affect each others functionality!

## Slide 8: Bluespec model needs to be extended to express Fifos with concurrent methods
EHR: Ephemeral History Registers

## Slide 9: EHR: Register with a bypass Interface
r0 < w0
D
Q
0
1
r0
w0.data
w0.en
w0 < r1
r1 – if write is not enabled it returns the current state and if write is enabled it returns the value being written
r1
normal
bypass

## Slide 10: Ephemeral History Register (EHR)
r0 < w0 < r1 < w1 < ….
D
Q
0
1
w0.data
w0.en
0
1
w1.data
w1.en
w[i+1] takes precedence over w[i]
Dan Rosenband [MEMOCODE’04]
r0
r1

## Slide 11: Designing FIFOs using EHRs

## Slide 12: One-Element Pipelined FIFO
module mkPipelineFifo(Fifo#(1, t)) provisos(Bits#(t, tSz));
Reg#(t) data <- mkRegU;
Ehr#(2, Bool) full <- mkEhr(False);
method Action enq(t x) if(!full[1]);
data <= x;
full[1] <= True;
endmethod
method Action deq if(full[0]);
full[0] <= False;
endmethod
method t first if(full[0]);
return data;
endmethod
endmodule
first < enq
deq < enq
first < deq
One can enq into a full Fifo provided someone is trying to deq from it simultaneously.
enq and deq calls can be from the same rule or different rules.

## Slide 13: One-Element Bypass FIFO using EHRs
module mkBypassFifo(Fifo#(1, t)) provisos(Bits#(t, tSz));
Ehr#(2, t) data <- mkEhr(?);
Ehr#(2, Bool) full <- mkEhr(False);
method Action enq(t x) if(!full[0]);
data[0] <= x;
full[0] <= True;
endmethod
method Action deq if(full[1]);
full[1] <= False;
endmethod
method t first if(full[1]);
return data[1];
endmethod
endmodule
enq < first
enq < deq
first < deq
One can deq from an empty Fifo provided someone is trying to enq into it simultaneously.
enq and deq calls can be from the same rule or different rules

## Slide 14: Two-Element Conflict-free FIFO
module mkCFFifo(Fifo#(2, t)) provisos(Bits#(t, tSz));
Ehr#(2, t) da <- mkEhr(?);
Ehr#(2, Bool) va <- mkEhr(False);
Ehr#(2, t) db <- mkEhr(?);
Ehr#(2, Bool) vb <- mkEhr(False);
rule canonicalize if(vb[1] && !va[1]);
da[1] <= db[1]; va[1] <= True; vb[1] <= False; endrule
method Action enq(t x) if(!vb[0]);
db[0] <= x; vb[0] <= True; endmethod
method Action deq if (va[0]);
va[0] <= False; endmethod
method t first if(va[0]);
return da[0]; endmethod
endmodule
Assume, if there is only one element in the FIFO it resides in da
db da
first CF enq
deq CF enq
first < deq
enq and deq, even if performed simultaneously, can’t see each other’s effects until the next cycle

## Slide 15: N-element Conflict-free FIFO
an enq updates enqP and puts the old value of enqP and enq data into oldEnqP and newData, respectively. It also sets enqEn to false to prevent further enqueues
a deq updates deqP and sets deqEn to false to prevent further dequeues
Canonicalize rule calculates the new count and puts the new data into the array and sets the enqEn and deqEn bits appropriately
enqP
deqP
enqEn
deqEn
oldEnqP
newData
locks for preventing accesses until canonicalization
temp storage to hold values until canonicalization

## Slide 16: Pointer comparison
enqP and deqP contain indices for twice the size of the FIFO, to distinguish between full and empty conditions
Full: enqP == deqP + FIFO_size
Empty: enqP == deqP

## Slide 17: N-element Conflict-free FIFO
module mkCFFifo(Fifo#(n, t))
provisos(Bits#(t, tSz), Add#(n, 1, n1), Log#(n1, sz), Add#(sz, 1, sz1));
Integer ni = valueOf(n); Bit#(sz1) nb = fromInteger(ni);
Bit#(sz1) n2 = 2*nb;
Vector#(n, Reg#(t)) data <- replicateM(mkRegU);
Ehr#(2, Bit#(sz1)) enqP <- mkEhr(0);
Ehr#(2, Bit#(sz1)) deqP <- mkEhr(0);
Ehr#(2, Bool) enqEn <- mkEhr(True);
Ehr#(2, Bool) deqEn <- mkEhr(False);
Ehr#(2, t) temp <- mkEhr(?);
Ehr#(2, Maybe#(Bit#(sz1))) tempEnqP <- mkEhr(Invalid);

## Slide 18: N-element Conflict-free FIFO continued-1
method Action enq(t x) if(enqEn[0]);
temp[0] <= x;
tempEnqP[0] <= Valid (enqP[0]%nb);
enqP[0] <= (enqP[0] + 1)%n2;
enqEn[0] <= False;
endmethod
method Action deq if(deqEn[0]);
deqP[0] <= (deqP[0] + 1)%n2; deqEn[0] <= False;
endmethod
method t first if(deqEn[0]);
return data[deqP[0]%nb];
endmethod

## Slide 19: N-element Conflict-free FIFO continued-2
rule canonicalize;
Bit#(sz1) cnt = enqP[1] >= deqP[1]?
enqP[1] - deqP[1]:
(enqP[1]%nb + nb) - deqP[1]%nb;
if(!enqEn[1] && cnt != nb) enqEn[1] <= True;
if(!deqEn[1] && cnt != 0) deqEn[1] <= True;
if(isValid(tempEnqP[1])) begin
data[validValue(tempEnqP[1])] <= temp[1];
tempEnqP[1] <= Invalid;
end
endrule
endmodule

## Slide 20: N-element searchable FIFO search CF {deq, enq}
module mkCFSFifo#(function Bool isFound(t v, st k))(SFifo#(n, t, st))
provisos(Bits#(t, tSz), Add#(n, 1, n1), Log#(n1, sz), Add#(sz, 1, sz1));
Integer ni = valueOf(n); Bit#(sz1) nb = fromInteger(ni);
Bit#(sz1) n2 = 2*nb;
Vector#(n, Reg#(t)) data <- replicateM(mkRegU);
Ehr#(2, Bit#(sz1)) enqP <- mkEhr(0);
Ehr#(2, Bit#(sz1)) deqP <- mkEhr(0);
Ehr#(2, Bool) enqEn <- mkEhr(True);
Ehr#(2, Bool) deqEn <- mkEhr(False);
Ehr#(2, t) temp <- mkEhr(?);
Ehr#(2, Maybe#(Bit#(sz1))) tempEnqP <- mkEhr(Invalid);
Ehr#(2, Maybe#(Bit#(sz1))) tempDeqP <- mkEhr(Invalid);
Need a tempDeqP also to avoid scheduling constraints between deq and Search

## Slide 21: N-element searchable FIFO search CF {deq, enq} continued-1
Bit#(sz1) cnt0 = enqP[0] >= deqP[0]? enqP[0] - deqP[0]:
(enqP[0]%nb + nb) - deqP[0]%nb;
Bit#(sz1) cnt1 = enqP[1] >= deqP[1]? enqP[1] - deqP[1]:
(enqP[1]%nb + nb) - deqP[1]%nb;
rule canonicalize;
if(!enqEn[1] && cnt2 != nb) enqEn[1] <= True;
if(!deqEn[1] && cnt2 != 0) deqEn[1] <= True;
if(isValid(tempEnqP[1])) begin
data[validValue(tempEnqP[1])] <= temp[1];
tempEnqP[1] <= Invalid;
end
if(isValid(tempDeqP[1])) begin
deqP[0] <= validValue(tempDeqP[1]); tempDeqP[1]<=Invalid;
end
endrule

## Slide 22: N-element searchable FIFO search CF {deq, enq} continued-2
method Action enq(t x) if(enqEn[0]);
temp[0] <= x; tempEnqP[0] <= Valid (enqP[0]%nb);
enqP[0] <= (enqP[0] + 1)%n2; enqEn[0] <= False;
endmethod
method Action deq if(deqEn[0]);
tempDeqP[0] <= Valid ((deqP[0] + 1)%n2);
deqEn[0] <= False;
endmethod
method t first if(deqEn[0]);
return data[deqP[0]%nb];
endmethod

## Slide 23: N-element searchable FIFO search CF {deq, enq} continued-3
method Bool search(st s);
Bool ret = False;
for(Bit#(sz1) i = 0; i < nb; i = i + 1)
begin
let ptr = (deqP[0] + i)%nb;
if(isFound(data[ptr], s) && i < cnt0)
ret = True;
end
return ret;
endmethod
endmodule

## Slide 24: Scheduling constraints due to multiple modules
rule ra;
aTob.enq(fa(x));
if (bToa.nonEmpty)
begin
x <= ga(bToa.first);
bToa.deq; end
endrule
rule rb;
bToa.enq(fb(y));
y <= gb(aTob.first);
aTob.deq;
endrule
aTob bToa Concurrent
fifo fifo scheduling?
CF CF
CF pipeline
CF bypass
pipeline CF
pipeline pipeline
pipeline bypass
bypass CF
bypass pipeline
bypass bypass
x


x
Can ra and rb be scheduled concurrently?
ra
rb
aTob
bToa
x
y
fifos are initially empty






## Slide 25: Register File: normal and bypass
Normal rf: {rd1, rd2} < wr; the effect of a register update can only be seen a cycle later, consequently, reads and writes are conflict-free
Bypass rf: wr < {rd1, rd2}; in case of concurrent reads and write, check if rd1==wr or rd2==wr then pass the new value as the result and update the register file, otherwise the old value in the rf is read

## Slide 26: Normal Register File
module mkRFile(RFile);
Vector#(32,Reg#(Data)) rfile <- replicateM(mkReg(0));
method Action wr(Rindx rindx, Data data);
if(rindx!=0) rfile[rindx] <= data;
endmethod
method Data rd1(Rindx rindx) = rfile[rindx];
method Data rd2(Rindx rindx) = rfile[rindx];
endmodule
{rd1, rd2} < wr
Notes: 26

## Slide 27: Bypass Register File using EHR
module mkBypassRFile(RFile);
Vector#(32,EHR#(2, Data)) rfile <-
replicateM(mkEHR(0));
method Action wr(Rindx rindx, Data data);
if(rindex!==0) rfile[rindex].r0(data);
endmethod
method Data rd1(Rindx rindx) = rfile[rindx].r1;
method Data rd2(Rindx rindx) = rfile[rindx].r1;
endmodule
wr < {rd1, rd2}
Notes: 27