## Slide 1
Computer Architecture: A Constructive Approach
Branch Prediction (2)
Derek Chiou
The University of Texas at Austin
Taken (with permission) from
Arvind
Computer Science & Artificial Intelligence Lab.
Massachusetts Institute of Technology

## Slide 2: Nomenclature
Drop an instruction: What we really mean is poison the instruction so that the subsequent stages know not to update any architectural state. The poisoned instruction has to be passed down for book keeping reasons, i.e., to remove it from the scoreboard.
Detecting a misprediction versus training/updating a predictor. On a pc misprediction, information about redirecting the pc has to be passed to the fetch stage. However for training the BTB and other predictors information has to be passed even when there is no misprediction.

## Slide 3: Overview of control prediction
Need
next PC immediately
Instr type, PC relative targets available
Simple conditions, register targets available
Complex conditions available
Next Addr
Pred
tight
loop
P C
Decode
Reg Read
Execute
Write
Back
Given (pc, ppc), a misprediction can be corrected (used to redirect the pc) as soon as it is detected. In fact, pc can be redirected as soon as we have a “better” prediction. However, for forward progress it is important that a correct pc should never be redirected.
mispred insts must be filtered
correct mispred
correct mispred
correct mispred
Notes: With respect to branches the important steps are…
With ‘stall style’ dependence resolution - correct next PC calculation waits for …
To alleviate stalls speculate next PC – now dependence info is speculation check

## Slide 4: Multiple Predictors
Suppose we maintain a table of how a particular Br has resolved before. At the decode stage we can consult this table to check if the incoming (pc, ppc) pair matches our prediction. If not redirect the pc
Need
next PC immediately
Instr type, PC relative targets available
Simple conditions, register targets available
Complex conditions available
Next Addr
Pred
tight
loop
P C
Decode
Reg Read
Execute
Write
Back
mispred insts must be filtered
Br Dir Pred
correct mispred
correct mispred

## Slide 5: Plan
Study several branch prediction schemes
Show how multiple corrections to the pc are made in the pipeline
Show how Branch-Direction Predictors are updated in the pipeline

## Slide 6: Next Address Predictor (NAP) first attempt
BP bits are stored with the predicted target address.
IF stage: nPC = If (BP=taken) then target else pc+4
later: check prediction, if wrong then kill the instruction
and update BTB & BPb else update BPb
iMem
PC
Branch
Target
Buffer
(2k entries)
k
BPb
predicted
target
BP
target

## Slide 7: Address Collisions
What will be fetched after the instruction at 1028?
NAP prediction =
Correct target =

Assume a
128-entry
NAP
BPb
target
take
236
1028 Add .....
132 Jump 100
Instruction
Memory
236
1032
kill PC=236 and fetch PC=1032
Is this a common occurrence?
Can we avoid these bubbles?

## Slide 8: Use NAP for Control Instructions only
NAP contains useful information for branch and
jump instructions only
 Do not update it for other instructions
For all other instructions the next PC is (PC)+4 !
How to achieve this effect without decoding the
instruction?

## Slide 9: Branch Target Buffer (BTB) a special form of NAP
Keep the (pc, predicted pc) in the BTB
pc+4 is predicted if no pc match is found
BTB is updated only for branches and jumps
2k-entry direct-mapped BTB
I-Cache
PC
k
Valid
valid
Entry PC (tag)
=
match
predicted
target
target PC
Permits nextPC to be determined before instruction is decoded

## Slide 10: Consulting BTB Before Decoding
1028 Add .....
132 Jump 100
BPb
target
take
236
entry PC
132
The match for pc =1028 fails and 1028+4 is fetched
   eliminates false predictions after ALU instructions
BTB contains entries only for control transfer instructions
   more room to store branch targets
Even very small BTBs are very effective

## Slide 11: Consulting BTB Before Decoding
1028 Add .....
132 Jump 100
target
236
entry PC
132
The match for pc =1028 fails and 1028+4 is fetched
 eliminates false predictions after ALU instructions
BTB contains entries only for control transfer instructions
   more room to store branch targets
Even very small BTBs are very effective

## Slide 12: Observations
Branch prediction’s importance grows with the instruction capacity of a processor pipeline
Processors often use more than one prediction scheme
It is usually easy to understand the data structures required to implement a particular scheme
It takes considerably more effort to understand how a particular scheme with its lookup and updates is integrated in the pipeline and how various schemes interact with each other

## Slide 13: Plan
Begin with a simple 2-stage pipeline and integrate a simple BTB scheme in it
Extend the design to a multistage pipeline and integrate at least one more predictor, say BHT, in the pipeline
revisit the simple two-stage pipeline without branch prediction

## Slide 14: 2-Stage-DH pipeline without Branch Predictor
PC
Inst
Memory
Decode
Register File
Execute
Data
Memory
itr
nextPC
fEpoch
eEpoch
stall
+4
Notes: 14

## Slide 15: 2-Stage-DH pipeline
module mkProc(Proc);
Reg#(Addr) pc <- mkRegU;
RFile rf <- mkBypassRFile;
IMemory iMem <- mkIMemory;
DMemory dMem <- mkDMemory;
SPipeReg#(TypeDecode2Execute) itr
<- mkSPipeReg(getDstE);
Reg#(Bool) fEpoch <- mkReg(False);
Reg#(Bool) eEpoch <- mkReg(False);
FIFOF#(TypeNextPCE)) nextPC
<- mkBypassFIFOF;
rule doFetch (itr.notFull); ... endrule
rule doExecute (itr.notEmpty); ... endrule
endmodule

## Slide 16: 2-Stage-DH pipeline doFetch rule
rule doFetch (itr.notFull);
let inst = iMem(pc);
let dInst = decode(inst);
let stall <- itr.search(dInst.src1, dInst.src2);
if(!stall) begin
let rVal1 = rf.rd1(fromMaybe(dInst.src1));
let rVal2 = rf.rd2(fromMaybe(dInst.src2));
itr.enq(TypeDecode2Execute{pc:pc,
epoch:fEpoch, dInst:dInst,
rVal1:rVal1, rVal2:rVal2});
if(nextPC.notEmpty) begin
npc = nextPC.first.npc;
nepoch = nextPC.first.nepoch;
pc <= npc; fEpoch <= nepoch; nextPC.deq;
end
else pc <= pc+4; end
endrule
Notes: 16

## Slide 17: 2-Stage-DH pipeline doExecute rule
rule doExecute (itr.notEmpty);
let itrpc=itr.first.pc; let dInst=itr.first.dInst;
let rVal1=itr.first.rVal1;
let rVal2=itr.first.rVal2;
if(itr.first.epoch==eEpoch) begin
let eInst = execute(dInst, rVal1, rVal2, itrpc);
let memData <- dMemAction(eInst, dMem);
regUpdate(eInst, memData, rf);
if(eInst.brTaken) begin
let nepoch = next(epoch); eEpoch <= nepoch;
nextPC.enq(
TypeNextPCE{npc:eInst.addr, nepoch:nepoch});
end
end
itr.deq;
endrule endmodule
Notes: 17

## Slide 18: 2-Stage-DH pipeline with a Branch Predictor
PC
Inst
Memory
Decode
Register File
Execute
Data
Memory
itr
nextPC
fEpoch
eEpoch
Branch
Predictor
stall
Notes: 18

## Slide 19: Branch Predictor Interface
interface NextAddressPredictor;
method Addr prediction(Addr pc);
method Action update(Addr pc,
Addr target);
endinterface

## Slide 20: Null Branch Prediction
module mkNeverTaken(NextAddressPredictor);
method Addr prediction(Addr pc);
return pc+4;
endmethod
method Action update(Addr pc, Addr target);
noAction;
endmethod
endmodule
Replaces PC+4 with …
  Already implemented in the pipeline
Right most of the time
  Why?
most instructions are not branches

## Slide 21: Branch Target Prediction (BTB)
module mkBTB(NextAddressPredictor);
RegFile#(LineIdx, Addr) tagArr <- mkRegFileFull;
RegFile#(LineIdx, Addr) targetArr <- mkRegFileFull;
method Addr prediction(Addr pc);
LineIdx index = truncate(pc >> 2);
let tag = tagArr.sub(index);
let target = targetArr.sub(index);
return (tag==tuncateLSB(pc) ? target : pc+4);
endmethod
method Action update(Addr pc, Addr target);
LineIdx index = truncate(pc >> 2);
tagArr.upd(index, truncateLSB(pc)); targetArr.upd(index, target);
endmethod
endmodule

## Slide 22: 2-Stage-DH pipeline + BTB
module mkProc(Proc);
Reg#(Addr) pc <- mkRegU;
RFile rf <- mkBypassRFile;
IMemory iMem <- mkIMemory;
DMemory dMem <- mkDMemory;
SPipeReg#(TypeDecode2Execute) itr
<- mkSPipeReg(getDstE);
Reg#(Bool) fEpoch <- mkReg(False);
Reg#(Bool) eEpoch <- mkReg(False);
FIFOF#(TypeNextPCE)) nextPC
<- mkBypassFIFOF;
NextAddressPredictor bpred <- mkNeverTaken;
typedef struct {
Addr pc; Addr ppc; Bool epoch; DecodedInst dInst;
Data rVal1; Data rVal2;
} TypeDecode2Execute deriving (Bits, Eq);

## Slide 23: 2-Stage-DH pipeline + BTB doFetch rule
rule doFetch (itr.notFull);
let inst = iMem(pc); let dInst = decode(inst);
let stall <- itr.search(dInst.src1, dInst.src2);
if(!stall) begin
let ppc = bpred.prediction(pc);
let rVal1 = rf.rd1(fromMaybe(dInst.src1));
let rVal2 = rf.rd2(fromMaybe(dInst.src2));
itr.enq(TypeDecode2Execute{pc:pc, ppc:ppc,
epoch:fEpoch, dInst:dInst,
rVal1:rVal1, rVal2:rVal2});
if(nextPC.notEmpty) begin
npc=nextPC.first.npc; nppc=nextPC.first.nppc;
nepoch=nextPC.first.nepoch;
pc <= nppc; fEpoch <= nepoch; nextPC.deq;
bpred.update(npc, nppc); end
else pc <= ppc; end
endrule
Notes: 23

## Slide 24: 2-Stage-DH pipeline + BP doExecute rule
rule doExecute (itr.notEmpty);
let itrpc=itr.first.pc; let dInst=itr.first.dInst;
let itrppc=itr.first.ppc; let rVal1=itr.first.rVal1;
let rVal2=itr.first.rVal2;
if(itr.first.epoch==eEpoch) begin
let eInst = execute(dInst, rVal1, rVal2,
itrpc, itrppc);
let memData <- dMemAction(eInst, dMem);
regUpdate(eInst, memData, rf);
if(eInst.misprediction) begin
let nepoch = next(epoch); eEpoch <= nepoch;
nextPC.enq(TypeNextPCE{npc: itrpc,
nppc: eInst.brTaken ? eInst.addr : itrpc+4,
nepoch:nepoch}); end end
itr.deq;
endrule endmodule
Notes: 24

## Slide 25: Execute Function
function ExecInst exec(DecodedInst dInst, Data rVal1,
Data rVal2, Addr pc, Addr ppc);
ExecInst eInst = ?;
let aluVal2 = (dInst.immValid)? dInst.imm : rVal2
let aluRes = alu(rVal1, aluVal2, dInst.aluFunc);
let brAddr = brAddrCal(pc, rVal1, dInst.iType,
dInst.imm);
eInst.itype = dInst.iType;
eInst.addr = (memType(dInst.iType)? aluRes : brAddr;
eInst.data = dInst.iType==St ? rVal2 : aluRes;
eInst.brTaken = aluBr(rVal1, aluVal2, dInst.brComp);
eInst.misprediction = eInst.brTaken ? brAddr!=ppc :
(pc+4)!=ppc;
eInst.rDst = dInst.rDst;
return eInst;
endfunction

## Slide 26: 3-Stage pipeline – 1 predictor
PC
Inst
Memory
Decode
Register File
Execute
Data
Memory
itr
nextPC
fEpoch
eEpoch
Branch
Predictor
stall
ir
nextPC
dEpoch
Notes: 26

## Slide 27: 3-Stage pipeline – 1 predictor
module mkProc(Proc);
Reg#(Addr) pc <- mkRegU;
RFile rf <- mkBypassRFile;
IMemory iMem <- mkIMemory;
DMemory dMem <- mkDMemory;
PipeReg#(TypeFetch2Decode) ir
<- mkPipeReg;
SPipeReg#(TypeDecode2Execute) itr
<- mkSPipeReg(getDstE);
Reg#(Bool) fEpoch <- mkReg(False);
Reg#(Bool) dEpoch <- mkReg(False);
Reg#(Bool) eEpoch <- mkReg(False);
FIFOF#(TypeNextPCE) nextPCE2D <- mkBypassFIFOF;
FIFOF#(TypeNextPCE) nextPCD2F <- mkBypassFIFOF;
NextAddressPredictor bpred <- mkNeverTaken;
Notes: 27

## Slide 28: 3-Stage pipeline – 1 predictor
rule doFetch (ir.notFull);
let inst = iMem(pc);
let ppc = bpred.prediction(pc);
ir.enq(TypeFetch2Decode{
pc:pc, ppc:ppc, epoch:fEpoch, inst:inst});
if(nextPCD2F.notEmpty) begin
npc=nextPC.first.npc; nppc=nextPC.first.nppc;
nepoch=nextPC.first.nepoch;
pc <= nppc; fEpoch <= nepoch; nextPC.deq;
bpred.update(npc, nppc);
end
else
pc <= ppc;
endrule
L17-28
Notes: 28

## Slide 29: 3-Stage pipeline – 1 predictor
rule doDecode (itr.notFull && ir.notEmpty);
let irpc=ir.first.pc; let irppc=ir.first.ppc;
let inst=ir.first.inst;
if(nextPCE2D.notEmpty) begin
dEpoch <= nextPCE2D.first.epoch;
nextPCD2F.enq(nextPCE2D.first);
nextPCE2D.deq; ir.deq; end
else if(ir.first.epoch==dEpoch) begin
let dInst = decode(inst);
let stall <- itr.search(dInst.src1, dInst.src2);
if(!stall) begin
let rVal1 = rf.rd1(validValue(dInst.src1));
let rVal2 = rf.rd2(validValue(dInst.src2));
itr.enq(TypeDecode2Execute{pc:irpc, ppc:irppc,
epoch:dEpoch, dInst:dInst, rVal1:rVal1, rVal2:rVal2});
ir.deq; end end
else ir.deq; endrule
L17-29
Notes: 29

## Slide 30: 3-Stage pipeline – 1 predictor
L17-30
rule doExecute (itr.notEmpty);
let itrpc=itr.first.pc; let dInst=itr.first.dInst;
let itrppc=itr.first.ppc; let rVal1=itr.first.rVal1;
let rVal2=itr.first.rVal2;
if(itr.first.epoch==eEpoch) begin
let eInst = execute(dInst, rVal1, rVal2,
itrpc, itrppc);
let memData <- dMemAction(eInst, dMem);
regUpdate(eInst, memData, rf);
if(eInst.misprediction) begin
let nepoch = next(epoch); eEpoch <= nepoch;
nextPCE2D.enq(TypeNextPCE{npc: itrpc,
nppc: eInst.brTaken ? eInst.addr : itrpc+4,
nepoch:nepoch}); end end
itr.deq;
endrule endmodule
Notes: 30

## Slide 31: N-Stage pipeline – BTB only
execRecirect
Execute
d2e
Decode
f2d
Fetch
PC
miss
pred?
fEpoch
At Execute:
  if !(epoch=eEpoch) then mark instruction as poisoned, send it to the latter stages so that scoreboard entry can be removed
  if no poisoning & mispred then change eEpoch; send <pc, newPc, ...> to Fetch
At Fetch:
  msg from execute: train BTB with <pc, newPc, taken, mispredict>
  if msg from execute indicates misprediction then set pc, change fEpoch
attached to every fetched instruction
{pc, ppc, epoch}
eEpoch
{pc, newPc, taken mispredict, ...}
BTB
...
Notes: 31
In a similar way to FXep and Xep, we distribute Dep into Dep and FDep.

## Slide 32: What Did We Learn?
Branch prediction strategies
How to implement in our system